## Slide 1
Reflections on flexibility in power price scenarios

## Slide 2
Internal Agenda
Webinar on September 18th, 2024
Review: Trend of Increasing Volatility in the Spot Market in Germany
Recap: Existing Flexibility Options and What We Need Them For
Outlook: Expected Development of Battery Storage, Heat Pumps, Electric Mobility, and Electrolyzer Capacity in Germany
Model Results: Improved Modelling of Flexible Demand and Results of Sample Years
Q&A

## Slide 3
Volatility in the Spot Market in Germany

## Slide 4
Power prices and PFC
Data source: Energy Brainpool with data from EEX/EPEX
Day-Ahead-Prices and Forward-Curve on trading day 28-08-2024
Notes: Volatility has increased compared to pre-crisis levels
During the crisis we had enourmous volatility but not only due to RE
\\BE-SRV-02\Projekte_intern\EB (Analysen - eigene)\EEX_Terminmarkt_Strom_SQL.xlsx
Von Marketing zuletzt geprüft: Oktober 2019
Zuletzt aktualisiert: 07.11.2022, MaB

## Slide 5
Daily Profile of Electricity Prices
Sources: EPEX Spot, own calculations
The daily structure of spot market prices has turned from a peak into a valley
Spread is now lower
Storage could run two cycles
Notes: \\BE-SRV-02\Projekte_intern\EB (Analysen - eigene)\EPEX_Spotpreis-Tagesprofile.xlsx
No peak at noon anymore
Dent/dip due to solar power is observable
Menti: What happens at wholesale market when more renewables are feeding into the grid?

## Slide 6
Price development - another perspective
Spot market prices for selected hours of the day
For 2024
Simple Moving Average
Spread between PV-peak and load-peak grows
?
Notes: Question: number of spot market prices

## Slide 7
Development of negative Prices
Source: EPEX Spot, own calculations
Notes: Almost 400 hours by today
Kernaussage:
Tonspur: 2020 was a year with lower demand (pandemic) and high RE feed-in, 2021 was a year with very low RE feed-in (especially from wind); perspective for the next years: fewer hours with negative spot prices as nuclear and coal exit progress and RE capacity needs time to catch up.
Interaktion (Menti/Whiteboard):
Quelle: \\BE-SRV-02\Projekte_intern\EB (Analysen - eigene)\POWER_SPOT_DA_negative_Preise.xlsb
Autor der Folie:
Zuletzt aktualisiert von/am: 17.01.2024, MaB
Hintergrundwissen:

## Slide 8
Price fluctuations in the spot market
Development of fluctuating renewables
Current PV / Wind on / Wind off: 92 / 62 / 9 GW
Target PV / Wind on / Wind off: 215 / 115 / 30 GW
Remuneration scheme does not incentivize reaction to low prices (60 GW PV with fixed FiT)
Flexible demand still limited:
  Battery storage
  Electrolyzers
  Heat pumps
  E-mobility
  Other flexible demand
Notes: Whiteboard: total peak demand vs. PV installed

## Slide 9
Examples of high volatility events
Volatility in the Spot Market in Germany
July 2nd, 2023 (solar excess): -500 EUR/MWh at DA Market
June 3rd, 2024 (flooding South Germany): +2000 EUR/MWh for ID1, over 9000 EUR/MWh for single bids, partly empty ask side
June 26th, 2024 (decoupling of markets): +2326 EUR/MWh at DA Market
?
Notes: June 2023; 28 GW solar generation when prices were down to -500, load 44-46 GW midday
Flooding: two waves of flooding in south Germany

## Slide 10
Existing Flexibility Options and What We Need Them For

## Slide 11
Balancing Supply and Demand
The bath tub + reserves

## Slide 12
Flexibility options
Flexibility options
Dispatchable generation
Hydro power & biogas
Hydrogen/gas turbines
Grids
Transmission grids & interconnectors
Distribution grids
Storage systems
Large-scale BESS
Home BESS
E-mobility (vehicle2grid)
Flexible demand
Electrolyzer
Heat pumps
E-mobility
other
Inflexible demand
Fluctuating renewable generation
Notes: Grid cross border capacity in 2024: approx 26 GW
Battery storage systems:

## Slide 13
Expected Development of Battery Storage, Heat Pumps, Electric Mobility, and Electrolyzer Capacity in Germany

## Slide 14
Expected Development:
Battery storage
Chart: 
| 47484 | 49310 | 50041 | 51136 | 52963 | 54789
germany ¦ nep_2023_c ¦ battery ¦ GW | 91.6 | 167.9
germany ¦ tyndp2024(final) nt40 ¦ battery ¦ GW | 109.812
germany ¦ tyndp2024(final) ga ¦ battery(prosumer) ¦ GW | 104.032 | 157.525 | 233.272
germany ¦ nep_2023_b ¦ battery ¦ GW | 91.1 | 141
germany ¦ nep_2023_a ¦ battery ¦ GW | 91.1 | 141
germany ¦ tyndp2024(final) nt30 ¦ battery ¦ GW | 3.2004
germany ¦ tyndp2024(final) de ¦ battery(prosumer) ¦ GW | 104.032 | 157.525 | 233.272
germany ¦ tyndp2024(final) nt ¦ battery ¦ GW | 3.2004 | 109.812
Notes: TYNDP – DE: Distributed Energy, GA: Global Ambition, NT: National Targets

## Slide 15
Expected Development:
Electrolyzer
Bureaucracy too difficult
PPAs difficult to find
Additionality and simultaneous production & consumption in question
Chart: 
| 47484 | 49310 | 50041 | 51136 | 52963 | 54789
germany ¦ tyndp2024(final) nt ¦ electrolyser ¦ GW | 12.789 | 35.0441
germany ¦ nep_2023_c ¦ electrolyser ¦ GW | 28 | 55
germany ¦ nep_2023_b ¦ electrolyser ¦ GW | 26 | 50
germany ¦ nep_2023_a ¦ electrolyser ¦ GW | 40 | 80
germany ¦ tyndp2024(final) ga ¦ electrolyser ¦ GW | 22.7118 | 36.789 | 83.6995
germany ¦ tyndp2024(final) de35 ¦ electrolyser ¦ GW | 21.0264
germany ¦ tyndp2024(final) de ¦ electrolyser ¦ GW | 21.0264 | 36.7887 | 78.9285
germany ¦ tyndp2024(final) nt30 ¦ electrolyser ¦ GW | 12.789
germany ¦ tyndp2024(final) nt40 ¦ electrolyser ¦ GW | 35.0441
germany ¦ tyndp2024(final) de50 ¦ electrolyser ¦ GW | 78.9285

## Slide 16
Expected Development:
Electric mobility
So far:
Germany as a late mover
No clear incentives, no passionate strategy, no effective support
Attempt to protect combustion engines
cars and charging stations: chicken and egg
Outlook:
Massive charging/discharging capacity
Temporary available, mobile
Chart: 
| 49310 | 51136 | 54789
germany ¦ tyndp2024(final) de ¦ battery(ev) ¦ GW | 1615.694 | 3163.101 | 4110.813
germany ¦ tyndp2024(final) ga ¦ battery(ev) ¦ GW | 1202.292 | 2437.47 | 3046.838

## Slide 17
Target Development:
Heat pumps
Current status
2019: 19 GW installed capacity
Governmental goal:
500,000 installations each year from 2024 onwards
Assumption: 10 kW on average
New installations achieved
2023: 356,000
H1-2024: 90,000
2024 (expected): 200,000
Chart: Installations
| 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039 | 2040 | 2041 | 2042 | 2043 | 2044 | 2045
annual installations | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000 | 500000
total no. of heat pumps | 500000 | 1000000 | 1500000 | 2000000 | 2500000 | 3000000 | 3500000 | 4000000 | 4500000 | 5000000 | 5500000 | 6000000 | 6500000 | 7000000 | 7500000 | 8000000 | 8500000 | 9000000 | 9500000 | 10000000 | 10500000 | 11000000
capacity in GW | 24 | 29 | 34 | 39 | 44 | 49 | 54 | 59 | 64 | 69 | 74 | 79 | 84 | 89 | 94 | 99 | 104 | 109 | 114 | 119 | 124 | 129
Sources: Bundesregierung /BMWK, ZDF, Statista
Notes: Compare 2040:
Batteries:
Ely: 40 GW
E-Mob: 3000 GW
HP: 110 GW

## Slide 18
Chart: Demand - GWh
| 43831 | 44197 | 44562 | 44927 | 45292 | 45658 | 46023 | 46388 | 46753 | 47119 | 47484 | 47849 | 48214 | 48580 | 48945 | 49310 | 49675 | 50041 | 50406 | 50771 | 51136 | 51502 | 51867 | 52232 | 52597 | 52963 | 53328 | 53693 | 54058 | 54424 | 54789 | 55154 | 55519 | 55885 | 56250 | 56615 | 56980 | 57346 | 57711 | 58076 | 58441
germany ¦ cen_q3-2024_final ¦ Demand_total ¦ GWh | 552468.989 | 565260.2389 | 547765.4229 | 521456.7396 | 520647.6445 | 548574.5226 | 578844.2575 | 607458.6029 | 635859.3069 | 663057.7744 | 683151.2949 | 685380.7638 | 689396.6063 | 688714.6668 | 691804.273 | 698213.9455 | 710792.0757 | 719424.5411 | 730298.6603 | 740298.4779 | 749735.7191 | 754920.4583 | 762948.7415 | 771623.8007 | 781782.7051 | 786675.7208 | 794191.7068 | 803084.6505 | 814443.9143 | 820990.0304 | 827883.5132 | 829863.0307 | 834842.0105 | 834727.5488 | 838019.9826 | 841331.7658 | 845109.0821 | 845758.8496 | 848836.3601 | 852075.7646 | 856625.7274
germany ¦ cen_q3-2024_final ¦ Demand_Heatpump ¦ GWh | 0 | 0 | 0 | 0 | 0 | 2332.9073 | 7516.8226 | 12700.7379 | 17951.9085 | 23082.7709 | 26858.8655 | 28914.4869 | 31080.6817 | 33031.3611 | 35086.9825 | 37506.9996 | 40516.6391 | 43245.5275 | 46110.8663 | 48976.205 | 52050.4749 | 54792.8497 | 57711.959 | 60631.0687 | 63775.9682 | 66465.546 | 69358.5692 | 72251.5926 | 75411.1246 | 78045.565 | 80938.5878 | 83831.611 | 87031.8337 | 89625.5837 | 92518.6068 | 95384.0471 | 98563.305 | 101055.2702 | 103887.0029 | 106718.7355 | 108656.5749
germany ¦ cen_q3-2024_final ¦ Demand_Ely ¦ GWh | 0 | 0 | 0 | 0 | 0 | 3995.7162 | 11837.8586 | 19664.1836 | 27538.8867 | 35364.2019 | 39727.5294 | 40843.4972 | 41951.4278 | 43077.3003 | 44190.4141 | 45261.8462 | 46290.0801 | 47322.929 | 48359.8742 | 49392.345 | 51041.4908 | 53267.0048 | 55498.0544 | 57717.9535 | 59943.0727 | 61692.7484 | 62982.4101 | 64265.2822 | 65556.0645 | 66848.3013 | 67916.9775 | 68775.2236 | 69632.3902 | 70495.6194 | 71351.1581 | 72653.8034 | 74369.6018 | 76082.7857 | 77792.951 | 79504.9541 | 80335.0073
germany ¦ cen_q3-2024_final ¦ Demand_Emob ¦ GWh | 0 | 0 | 0 | 0 | 0 | 21972.7414 | 31213.123 | 40488.0861 | 49888.5624 | 58973.23 | 65591.5434 | 69575.3952 | 73805.6509 | 77601.863 | 81574.2725 | 86286.9498 | 92028.1262 | 97311.4496 | 102897.8355 | 108390.3512 | 111806.0665 | 112280.0439 | 113073.6687 | 113867.2933 | 115102.3492 | 115471.8805 | 116160.9728 | 116894.2082 | 117921.6963 | 118453.611 | 119165.0554 | 119876.0785 | 120865.0567 | 121298.5498 | 122031.7871 | 122825.1656 | 123822.8713 | 124062.342 | 124726.7432 | 125391.1443 | 126134.4535
germany ¦ cen_q3-2024_final ¦ Demand_applied ¦ GWh | 552468.989 | 565260.2389 | 547765.4229 | 521456.7396 | 520647.6445 | 520273.1577 | 528276.4534 | 534605.5953 | 540479.9493 | 545637.5717 | 550973.3567 | 546047.3845 | 542558.846 | 535004.1424 | 530952.6039 | 529158.15 | 531957.2303 | 531544.6349 | 532930.0843 | 533539.5766 | 534837.687 | 534580.5599 | 536665.0593 | 539407.4851 | 542961.3151 | 543045.5458 | 545689.7547 | 549673.5675 | 555555.0289 | 557642.5531 | 559862.8925 | 557380.1175 | 557312.73 | 553307.7958 | 552118.4306 | 550468.7496 | 548353.3041 | 544558.4518 | 542429.6631 | 540460.9307 | 541499.6917
Total demand in our power price scenarios
Policy developments driving these changes?
EU Level
  National Level
    Local Level
?
Notes: Is our path correct?

## Slide 19
Improved Modelling of Flexible Demand in Power Price Scenarios

## Slide 20
Model Structure & Functionality
EU-27 +
CH, NO, GB

## Slide 21
Scenario Overview:
Developments in Europe
Scenario | Renewable energies | Commodity prices | CO2 prices | Nuclear power stations | Coal fired power stations | E-mobility and PV-storage systems | Share of power generation in 2050 (2060) Emission free Renewables
„Central“ |  |  |  |  |  |  | 94 % (100 %) 76 % (77 %)
„Tensions“ |  |  |  |  |  |  | 90 % (94 %) 74 % (75 %)
„GoHydrogen“ |  |  |  |  |  |  | 100 % (100 %) 82 % (82 %)
Stable
Decrease, strong decrease
Strong increase
Increase
?
Notes: In the "Central"scenario, it is assumed that as a result of the current tensions with Russia, Europe will stop importing Russian pipeline gas by 2027 at the latest. From 2027 onwards, the price of natural gas in Europe is determined by the world market price for LNG. In the long run, fossil natural gas will be substituted by synthetic fuels and in particular green hydrogen. The prices for hard coal, oil and EUAs are based on the „Announced Pledges“ scenario of the „World Energy Outlook 2023“, in particular with increasing CO₂ prices until 2050.
For the short-term price paths of fuel and CO₂ , the developments on the futures markets caused by the geopolitical situation are taken into account.
The scenario assumes a strongly decentralized energy system in the future with a considerable expansion of renewables, to reduce Europe's general dependence on fossil fuels imports in the medium run, and to eliminate it as soon as possible. This expansion is accompanied by an increase in the flexible demand for electricity.
The scenario „Tensions“ assumes that the current tensions between Russia and the west will continue and intensify in the coming years. As a consequence, Europe stops the imports of Russian pipeline gas as early as possible. The price of natural gas is subsequently determined by the world market price for LNG. European consumers are competing for LNG with Asian markets, which leads to a high natural gas price level also in the medium run.
The prices for hard coal, oil and EUAs are based on the „Stated Policies“ (coal and oil) and „Net Zero Emissions by 2050“ (EUAs) scenarios of the „World Energy Outlook 2023“. A sharp increase in CO₂ prices until 2050 is assumed both to generate additional revenues to refinance government debt, and to promote technological development for the applications of hydrogen.
In certain countries, for example in Germany, the scenario assumes a slower expansion of renewables than in the „Central“ scenario, due to skilled labour shortages and a lack of political support.
In the "GoHydrogen" scenario, it is assumed that the goal of Europe-wide climate neutrality by 2050 according to the EU Green Deal is achieved through the use of green hydrogen - as one of the main energy carriers in industry, transport and buildings. Electrification and the increased use of electrolysers to meet the demand for hydrogen will greatly increase the demand for electricity. This is mainly compensated by the expansion of renewables. With regard to commodity prices, a continuously rising price for CO2 emission certificates is the key element to create incentives for CO2-neutral technologies. After climate neutrality has been achieved, this price will be kept at a high level to penalise further CO2 emissions. Fossil natural gas is gradually replaced by hydrogen between 2030 and 2040, so that the gas price after 2040 is related to the world market price for green hydrogen. Since the other fossil fuels play a minor role in the GoHydrogen scenario, a strongly falling trend is assumed for the prices of hard coal and oil according to the "Net Zero Emissions" of the "World Energy Outlook 2023".

## Slide 22
Recent changes
Revised modelling approach for Nordic price zones: Denmark, Norway and Sweden include zone-specific modelling. The individual bidding zones of Denmark (DK1 and DK2), Norway (NO1 to NO5) and Sweden (SE1 to SE4) are modelled as separate markets in our electricity price scenarios.
Country-specific updates to the assumptions for the Nordics and Eastern Europe: In Northern and Eastern Europe, the assumptions for emission-free generation technologies (nuclear, renewables and H2-ready gas turbines) and flexible demand have been adjusted in line with new government statements on energy policy.
Revised flexible demand modelling: Our approach to modelling flexible demand includes the future development of heat pumps, electrolysers and electric vehicles separately.
Notes: Revised modelling approach for Nordic price zones: From this update, all our country reports for Denmark, Norway and Sweden include zone-specific modelling. The individual bidding zones of Denmark (DK1 and DK2), Norway (NO1 to NO5) and Sweden (SE1 to SE4) are now modelled as separate markets in our electricity price scenarios. Due to temporary interruptions in domestic transmission capacities, particularly in Sweden and Norway, there have been significant zonal price differences in the Day-Ahead market in recent years.
Country-specific updates to the assumptions for the Nordics and Eastern Europe: In Northern and Eastern Europe, the assumptions for emission-free generation technologies (nuclear, renewables and H2-ready gas turbines) and flexible demand have been adjusted in line with new government statements on energy policy. There is currently a recognisable trend in many countries that the expansion of renewables (especially solar and wind) is no longer being pushed as progressively as before in the new government declarations, but rather the expansion of emission-free conventional generation capacities such as nuclear power and gas turbines is being discussed.
Revised flexible demand modelling: Our approach to modelling flexible demand includes the future development of heat pumps, electrolysers and electric vehicles. The further development of this approach can better reflect the different degrees of flexibility of these three applications.

## Slide 23
a. 50% lower
Let‘s play!
What would happen to the power price, if flexible demand was…
Chart: 
| 45658 | 46023 | 46388 | 46753 | 47119 | 47484 | 47849 | 48214 | 48580 | 48945 | 49310 | 49675 | 50041 | 50406 | 50771 | 51136 | 51502 | 51867 | 52232 | 52597 | 52963 | 53328 | 53693 | 54058 | 54424 | 54789
Cental | 76.2197 | 69.3712 | 62.7406 | 70.306 | 77.2346 | 78.3611 | 76.2159 | 69.5979 | 69.3166 | 64.0555 | 60.6983 | 57.813 | 57.0036 | 56.0783 | 56.6923 | 53.4967 | 52.7734 | 54.3679 | 55.2161 | 55.8606 | 56.8158 | 56.4365 | 56.0366 | 57.1311 | 62.2885 | 62.5413
High Flex (+50%) | 77.2506 | 69.8406 | 61.957 | 64.0536 | 73.2304 | 73.1939 | 68.8442 | 64.435 | 60.8538 | 57.2579 | 56.0992 | 52.8122 | 52.3423 | 51.8592 | 52.6048 | 49.5966 | 48.6021 | 50.2045 | 51.9326 | 51.5794 | 52.8968 | 52.1951 | 53.0332 | 53.7435 | 58.8932 | 60.0431
Low Flex (-50%) | 77.7764 | 71.7177 | 66.0879 | 78.681 | 85.3042 | 92.6764 | 93.39 | 78.2473 | 76.1572 | 68.8124 | 60.0151 | 58.1954 | 57.8699 | 57.2719 | 58.8279 | 53.8154 | 53.9292 | 54.9095 | 55.7472 | 55.5897 | 57.4022 | 56.4893 | 57.5738 | 58.1677 | 62.5912 | 63.3686
5 to 10 % reduction of power prices
Next 10 years: power prices increase significantly
Beyond 2035: almost no change in power prices
b. 50% higher

## Slide 24
Reasons for price variatons
2030: variation of prices especially in winter
Due to days/weeks with darkness + no wind (Dunkelflaute)
With Low-Flex, more generation from expensive generation or imports needed
2040: variation of prices especially in summer
With High-Flex, more power shifted to low-price hours (PV peak hours)
With Low-Flex, less power shifted to low-price hours (PV peak hours)
Chart: 
| 47119 | 47150 | 47178 | 47209 | 47239 | 47270 | 47300 | 47331 | 47362 | 47392 | 47423 | 47453 | 47484 | 47515 | 47543 | 47574 | 47604 | 47635 | 47665 | 47696 | 47727 | 47757 | 47788 | 47818 | 47849 | 47880 | 47908 | 47939 | 47969 | 48000 | 48030 | 48061 | 48092 | 48122 | 48153 | 48183
Cental | 95.8123 | 91.4204 | 71.515 | 62.9581 | 43.784 | 48.4885 | 52.6313 | 63.966 | 63.3815 | 78.4066 | 70.6331 | 183.1437 | 116.9475 | 106.7997 | 75.3484 | 66.727 | 39.8162 | 45.6223 | 51.2383 | 62.3259 | 63.7259 | 81.3883 | 69.994 | 160.9779 | 126.6044 | 104.4784 | 76.862 | 65.5222 | 33.9198 | 40.6198 | 44.4977 | 56.7805 | 61.8093 | 79.641 | 66.9929 | 157.343
High Flex (+50%) | 96.8716 | 90.3806 | 71.427 | 63.0246 | 39.5909 | 46.503 | 50.401 | 62.217 | 62.2089 | 78.6713 | 69.5661 | 147.8976 | 107.7606 | 100.7868 | 75.4116 | 63.8269 | 35.6926 | 40.7003 | 45.1709 | 58.6732 | 61.789 | 80.473 | 68.6523 | 140.1948 | 108.9865 | 104.1119 | 74.8584 | 63.1023 | 28.1251 | 32.2899 | 38.5106 | 51.5088 | 59.3812 | 78.8583 | 65.8221 | 122.2215
Low Flex (-50%) | 98.9068 | 115.6342 | 68.37 | 60.621 | 38.7449 | 45.4472 | 49.6702 | 60.8238 | 60.1978 | 96.6942 | 100.7233 | 228.3581 | 164.2124 | 177.1923 | 72.9402 | 62.959 | 37.1845 | 41.5242 | 47.7698 | 60.6546 | 60.4955 | 115.929 | 94.621 | 181.2297 | 198.1207 | 186.4467 | 73.6456 | 62.0921 | 30.3061 | 36.6638 | 42.4365 | 55.1752 | 58.4222 | 86.7313 | 102.4225 | 193.5464
Chart: 
| 50771 | 50802 | 50830 | 50861 | 50891 | 50922 | 50952 | 50983 | 51014 | 51044 | 51075 | 51105 | 51136 | 51167 | 51196 | 51227 | 51257 | 51288 | 51318 | 51349 | 51380 | 51410 | 51441 | 51471 | 51502 | 51533 | 51561 | 51592 | 51622 | 51653 | 51683 | 51714 | 51745 | 51775 | 51806 | 51836
Cental | 103.0218 | 97.2389 | 69.5989 | 51.9867 | 19.1418 | 20.3853 | 18.2997 | 27.5679 | 28.8211 | 53.1161 | 56.299 | 136.5194 | 102.5495 | 100.0294 | 67.3203 | 50.9176 | 15.1873 | 18.7078 | 14.5992 | 22.0562 | 24.9604 | 52.8354 | 61.1609 | 112.7592 | 103.0283 | 100.1763 | 67.1987 | 48.7869 | 17.8533 | 13.6103 | 15.077 | 20.7715 | 25.6419 | 49.9456 | 56.3452 | 117.2808
High Flex (+50%) | 104.3681 | 98.8556 | 70.0598 | 47.7584 | 13.2979 | 11.5339 | 9.5247 | 15.9158 | 21.1063 | 49.3714 | 57.2879 | 134.308 | 105.5279 | 101.1287 | 66.1714 | 44.7209 | 9.6813 | 9.253 | 7.063 | 12.709 | 18.3886 | 49.5852 | 59.3556 | 112.7488 | 105.4183 | 101.5997 | 66.6123 | 43.8827 | 11.9074 | 5.4163 | 7.1235 | 8.3841 | 18.5484 | 45.9258 | 55.2081 | 116.0262
Low Flex (-50%) | 106.2574 | 96.7746 | 65.5181 | 50.0089 | 20.993 | 22.2716 | 21.77 | 30.7579 | 30.0132 | 50.8876 | 56.1502 | 155.7254 | 100.107 | 97.7737 | 61.9843 | 48.3626 | 17.7329 | 21.384 | 18.3201 | 25.9923 | 26.3742 | 50.982 | 58.6446 | 119.0113 | 105.701 | 98.78 | 62.8147 | 47.3415 | 20.2099 | 17.4081 | 19.5489 | 25.7783 | 27.8635 | 48.9396 | 51.921 | 122.8878
Notes: Key figures to add:
2030: up to 40-50% higher prices in some winter months if flex-demand is 50% lower
2040: up to 50% lower prices in some summer months if flex-demand is 50% higher

## Slide 25
Scenario-Swarm to Quantify „known unknowns“
1000 Scenario Runs around a basis scenario
Known unkowns:
Weather
Market volatility (economic upswings and shocks, commodities)
Beyond long-term trends, we know there will be volatility (e.g. 2020 vs. 2021)
Notes: Die Strompreisszenarien in den BrainReports sind eine Mittelwertschätzung (Median/P-50), für ein gegebenes Set an Input-Parametern; aber wie hoch ist das Preisrisiko? Wie hoch oder niedrig können Strompreise ausfallen, wenn es anders kommt, und was sind die damit einhergehenden Wahrscheinlichkeiten?
  Monte Carlo Simulation mit ~3000 Szenarioläufen.
  Die Modelparameter (Wetterjahre, Stromnachfrage, Rohstoffpreise) werden für jeden Lauf aus einer gegebenen Verteilung zufällig gewählt.
  Auf diese Weise können wir Aussagen treffen über die zukünftige Verteilung von Strompreisen, Vermarktungswerten und –mengen, Extrempreisen etc., sowie Abschätzungen hinsichtlich eines „low case“ (z.B. P-90) machen.
Calculation of scenario-swarm with n = 1.000 each scenario
For every n:
  Choose a random* sequence of weather years
  Choose a random* sequence of deviations of commodity-price-trend
  Choose a random* deviation of electricity demand
Evaluate every single scenario and use the scattering of results to generate probabilities

## Slide 26
Energy BrainSwarms: Methodological Approach
Simulation run #1000
Simulation run #…
Simulation run #2
Simulation run #1
Randomly drawn
model parameters
Fundamental Scenario-swarm simulation
Distributions
Commodity prices
Power demand
Weather years
“short-term noise“…
…within the pillars of a future energy system

## Slide 27
What questions do you have?

## Slide 28
Thank you!
Matthis Brinkhaus
Senior Expert
Energy Brainpool – part of the Montel Group
Matthis.Brinkhaus@montelgroup.com
+49 162 9295900